## Slide 1
Kai wei Cheng ouyang
EEL 5934
Trajectory tracking sliding mode control of underactuated AUV

## Slide 2: Background
Autonomous underwater vehicles (AUVs) play a major role in the exploration of oceans, and in scientific and military missions. These vehicles are required to execute different types of missions without the interaction of human operators while performing well under a variety of load conditions and with unknown sea currents.
Motion control of AUVs may have different control objectives such as trajectory tracking, path following and way-point tracking. The trajectory tracking refers to the design of control laws so that the vehicle tracks a desired, time-parametrized trajectory, while the path following requires the path to be independent of time and is expressed in terms of its geometric description

## Slide 3: What we do
Designing a nonlinear motion controller for an autonomous underwater vehicle to track an arbitrary trajectory. The trajectory is assumed to be smooth and bounded.
The stability of the tracking system should proved and validated through simulations. The controller should be tuned to achieve good performance and reasonable settling times.

## Slide 4: Related works & Refferences
[1] Elmokadem, Taha, Mohamed Zribi, and Kamal Youcef-Toumi. "Trajectory tracking sliding mode control of underactuated AUVs."
Encountered the sliding mode surface oscillation problem. We replaced the discontinuous function sign with the continuous function tanh, thus eliminating the problem of oscillation .
Challenge

## Slide 5: 6 degrees of freedom
the surge (longitudinal motion)
the sway (lateral motion)
the yaw (rotation about the vertical axis)
heave (vertical motion)
the roll (rotational motion about the longitudinal axis)
the pitch (rotational motion about the lateral axis)

## Slide 6: Kinematic equations
x and y: coordinates of the vehicle's center of mass
: orientation
u: surge linear velocities of the vehicle
v: sway linear velocities of the vehicle
r: vehicle’s yaw angular velocity
: surge force, control input
: yaw moment, control input

## Slide 7: Define tracking errors
Position tracking errors:
Velocity tracking errors:
We want to let x – xd = 0, y– yd = 0, this means that the auv moves along the trajectory we want

## Slide 8: A block diagram of the AUV’s trajectory tracking control system

## Slide 9: Desired velocities design
Let the desired surge and sway velocities be such that,
Then, we can get the following:

## Slide 10: Trajectory tracking SMC design
We will choose the sliding surfaces such that:
We will choose the reaching law such that:

## Slide 11
the trajectory tracking surge and yaw control laws are chosen such that:
where,

## Slide 12: Lyapunov-Based Stability Analysis
Lyapunov function:
The time derivative of

## Slide 13
On the sliding surface, we can get:
Since , and are chosen to be positive scalars, the dynamics ensure the asymptotic convergence of ( , ) to (0, 0).

## Slide 14
According to this function:
We can get

## Slide 15
Lyapunov function:
The time derivative of

## Slide 16: Simulation result
Fig1. The actual and desired paths of the AUV
Fig2. The position tracking errors of the AUV

## Slide 17
Fig3. The velocity tracking errors of the AUV
Fig4. The surge and yaw control laws of the AUV

## Slide 18
Fig5. The actual and desired paths of the AUV
Fig6. The position tracking errors of the AUV

## Slide 19
Fig7. The velocity tracking errors of the AUV
Fig8. The surge and yaw control laws of the AUV

## Slide 20
Fig9. The actual and desired paths of the AUV
Fig10. The position tracking errors of the AUV

## Slide 21
Fig11. The velocity tracking errors of the AUV
Fig12. The surge and yaw control laws of the AUV

## Slide 22: Robustness Studies
The new AUV kinematic and dynamic equations are,

## Slide 25: Conclusion
A trajectory tracking sliding mode control scheme is proposed for the control of the lateral motion of AUVs.
The objective of this controller is to force the position of the AUV to track a desired, time-varying trajectory.
The control design is validated by applying it to an AUV and simulating its performance for different cases of reference trajectories.
the proposed control scheme works well for the three different cases.
the proposed control scheme is robust to bounded disturbances.

## Slide 26
Thanks!